QUADRAVERB PLUS MIDI IMPLEMENTATION

SYSTEM EXCLUSIVE FORMAT

The QuadraVerb MIDI System Exclusive message format is as follows:

F0		System exclusive status

00 00 0E	Alesis manufacturer id#

02		Quadraverb id#

cc		Opcode

dd		Data

:		    :

:		    :

F7		End-Of-Exclusive

OPCODES:

01  -  MIDI Editting

F0 00 00 0E 02 01<function#><page#>< value1>< value2>< value3>F7

<function#> 	=   1=reverb, 2=delay, 3=pitch, 4=eq, 7=config, 8=mix, 9=mod, 10=name

<page#>       	=  0..n       where n is the maximum page # for the selected function

<value1-3>	=  new parameter value in the following format:

Data:  B7 B6 B5 B4 B3 B2 B1 B0   (MSB)

A7 A6 A5 A4 A3 A2 A1 A0   (LSB)

Sent:   0   A7 A6 A5 A4 A3 A2 A1   <value1>

0   A0 B7 B6 B5 B4 B3 B2   <value2>

0   B1 B0  0    0    0    0   0    <value3>

All parameters to be edited must be sent in this format (12 MIDI bytes), regardless of the number of bits required to transmit the value of the parameter.  When the QuadraVerb receives this message, it will edit the specified parameter to the new value and display it.  If the function and page selected does not exist in the current configuration, the command will be ignored.  If the value received is out of range for the parameter selected, the range will be limited to a legal value.  The function and page numbers for each parameter are shown in the next section.

02  -  MIDI Data Dump 	F0 00 00 0E 02 02 <program#> <data> F7

<program#>	=  0..99 selects individual programs

=  100 selects the edit buffer

=  > 100  selects all 100 programs

<data> is in a packed format in order to optimize data transfer.  Eight MIDI bytes are used to transmit each block of 7 QuadraVerb data bytes.  If the 7 data bytes are looked at as one 56-bit word, the format for transmission is eight 7-bit words beginning with the most significant bit of the first byte, as follows:

SEVEN QUADRAVERB BYTES:

0: A7 A6 A5 A4 A3 A2 A1 A0

1: B7 B6 B5 B4 B3 B2 B1 B0

2: C7 C6 C5 C4 C3 C2 C1 C0

3: D7 D6 D5 D4 D3 D2 D1 D0

4: E7 E6 E5 E4 E3 E2 E1 E0

5: F7 F6 F5 F4 F3 F2 F1 F0

6: G7 G6 G5 G4 G3 G2 G1 G0

TRANSMITTED AS:

0: 0 A7 A6 A5 A4 A3 A2 A1

1: 0 A0 B7 B6 B5 B4 B3 B2

2: 0 B1 B0 C7 C6 C5 C4 C3

3: 0 C2 C1 C0 D7 D6 D5 D4

4: 0 D3 D2 D1 D0 E7 E6 E5

5: 0 E4 E3 E2 E1 E0 F7 F6

6: 0 F5 F4 F3 F2 F1 F0 G7

7: 0 G6 G5 G4 G3 G2 G1 G0

There are 147 bytes sent for a single data dump, which corresponds to 128 bytes of program data.  There are 14,629 bytes sent for a 100 program dump, which corresponds to 12,800 bytes of program data.  The location of each parameter within a program is shown in the next section.

When the QuadraVerb receives a data dump message, the display reads:

LOADING

MIDI DATA ...

Should the Quadraverb's MIDI input buffer overflow, the display will read:

MIDI INPUT

BUFFER OVERFLOW

This message will remain on the display until any button is pressed.

03  -  MIDI Dump Request

F0 00 00 0E 02 03 <program#> F7

<program#>	=  0..99 selects individual programs

=  100 selects the edit buffer

=  > 100  selects all 100 programs

When this message is received, a MIDI data dump will be initiated, and the display will read:

MIDI DATA DUMP

IN PROGRESS

Upon completion of the dump, the display will return to its previously displayed page.

INDIVIDUAL PARAMETER LOCATION FUNCTION AND PAGE VALUES

The following lists give the parameter locations and ranges for each of the effects in each of the configurations.  The parameter associated with a particular function and page may be dependent on both the current configuration, and the current mode of the effect (e.g., chorus, phase, etc.).  In conditions where a page relates to different parameters depending on the mode of the effect, the parameters are listed in tables under each mode.  All parameters are offset binary values.  This means that a signed parameter with a range of -99 to +99 in the display is actually stored as 0 for -99, 99 for 0, and 198 for +99.

REVERB (FUNCTION 1)

CONFIGURATION 0, 5, & 6:

page

0 (type)  0 (PLATE 1)		1 (ROOM 1)	2 (CHAMBER 1)	3 (HALL 1)	4 (REVERSE 1)

1	  0-3 (INPUT 1)	0-3 (INPUT 1)	0-3 (INPUT 1)	0-3 (INPUT 1)	0-3 (INPUT 1)

2	0-1 (INPUT 2)	0-1 (INPUT 2)	0-1 (INPUT 2)	0-1 (INPUT 2)	0-1 (INPUT 2)

3	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)

4	1-140 (PREDLY)	1-140 (PREDLY)	1-140 (PREDLY)	1-140 (PREDLY)	1-140 (PREDLY)

5	1-198 (PRE MIX)	1-198 (PRE MIX)	1-198 (PRE MIX)	1-198 (PRE MIX)	1-198 (PRE MIX)

6	0-99 (DECAY)	0-99 (DECAY)	0-99 (DECAY)	0-99 (DECAY)	0-99 (REV TIME)

7	0-8 (DIFFUSION)	0-8 (DIFFUSION)	0-8 (DIFFUSION)	0-8 (DIFFUSION)	0-8 (DIFFUSION)

8	0-8 (DENSITY)	0-8 (DENSITY)	0-8 (DENSITY)	0-60 (LOW DEC)	0-8 (DENSITY)

9	0-60 (LOW DEC)	0-60 (LOW DEC)	0-60 (LOW DEC)	0-60 (HIGH DEC)	0-60 (LOW DEC)

10	0-60 (HIGH DEC)	0-60 (HIGH DEC)	0-60 (HIGH DEC)	0-1 (GATE ON)	0-60 (HIGH DEC)

11	0-1 (GATE ON)	0-1 (GATE ON)	0-1 (GATE ON)	0-99 (GATE HLD)

12	0-99 (GATE HLD)	0-99 (GATE HLD)	0-99 (GATE HLD)	0-99 (GATE REL)

13	0-99 (GATE REL)	0-99 (GATE REL)	0-99 (GATE REL)	0-99 (GATE LEV)

14	0-99 (GATE LEV)	0-99 (GATE LEV)	0-99 (GATE LEV)

CONFIGURATION 1:

page

0 (type)	0 (PLATE 1)	1 (ROOM 1)	2 (CHAMBER 1)	3 (HALL 1)	4 (REVERSE 1)

1	0-2 (INPUT 1)	0-2 (INPUT 1)	0-2 (INPUT 1)	0-2 (INPUT 1)	0-2 (INPUT 1)

2-14 same as configuration 0

CONFIGURATION 2, 3 & 7:

Not used

CONFIGURATION 4:

page

0 (type)	0 (PLATE 2)	1 (ROOM 2)	2 (CHAMBER 2)	3 (HALL 2)	4 (REVERSE 2)

1	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)

2	1-140 (PREDLY)	1-140 (PREDLY)	1-140 (PREDLY)	1-140 (PREDLY)	1-140 (PREDLY)

3	1-198 (PRE MIX)	1-198 (PRE MIX)	1-198 (PRE MIX)	1-198 (PRE MIX)	1-198 (PRE MIX)

4	0-99 (DECAY)	0-99 (DECAY)	0-99 (DECAY)	0-99 (DECAY)	0-99 (REV TIME)

5	0-8 (DIFFUSION)	0-8 (DIFFUSION)	0-8 (DIFFUSION)	0-8 (DIFFUSION)	0-8 (DIFFUSION)

6	0-8 (DENSITY)	0-8 (DENSITY)	0-8 (DENSITY)	0-60 (LOW DEC)	0-8 (DENSITY)

7	0-60 (LOW DEC)	0-60 (LOW DEC)	0-60 (LOW DEC)	0-60 (HIGH DEC)	0-60 (LOW DEC)

8	0-60 (HIGH DEC)	0-60 (HIGH DEC)	0-60 (HIGH DEC)	0-1 (GATE ON)	0-60 (HIGH DEC)

9	0-1 (GATE ON)	0-1 (GATE ON)	0-1 (GATE ON)	0-99 (GATE HLD)

10	0-99 (GATE HLD)	0-99 (GATE HLD)	0-99 (GATE HLD)	0-99 (GATE REL)

11	0-99 (GATE REL)	0-99 (GATE REL)	0-99 (GATE REL)	0-99 (GATE LEV)

12	0-99 (GATE LEV)	0-99 (GATE LEV)	0-99 (GATE LEV)

DELAY (FUNCTION 2)

CONFIGURATION 0:

page

0 (type)	0 (MONO)	1 (STEREO)	2 (PING-PONG)

1	0-1 (INPUT 1)	0-1 (INPUT 1)	0-1 (INPUT 1)

2	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)

3	1-800 (DELAY)	1-400 (L DELAY)	1-400 (DELAY)

4	0-99 (FEEDB)	0-99 (L FEEDB)	0-99 (FEEDB)

5		1-400 (R DELAY)

6		0-99 (R FEEDB)

CONFIGURATION 1, 5:

page

0 (type)	0 (MONO)	1 (STEREO)	2 (PING-PONG)

1	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)

2	1-800 (DELAY)	1-400 (L DELAY)	1-400 (DELAY)

3	0-99 (FEEDB)	0-99 (L FEEDB)	0-99 (FEEDB)

4		1-400 (R DELAY)

5		0-99 (R FEEDB)

CONFIGURATION 2:

page

0 (type)	0 (MONO)	1 (STEREO)	2 (PING-PONG)

1	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)

2	1-1500 (DELAY)	1-750 (L DELAY)	1-750 (DELAY)

3	0-99 (FEEDB)	0-99 (L FEEDB)	0-99 (FEEDB)

4		1-750 (R DELAY)

5		0-99 (R FEEDB)

CONFIGURATION 3:

page

0 (type)	0 (MONO)	1 (STEREO)	2 (PING-PONG)	3 (MULTI-TAP)

1	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)

2	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)

3	1-1500 (DELAY)	1-750 (L DELAY)	1-750 (DELAY)	0-7 (TAP NUMBER)

4	0-99 (FEEDB)	0-99 (L FEEDB)	0-99 (FEEDB)	1-1493 (TAP DELAY)

5		1-750 (R DELAY)		0-99 (TAP VOLUME)

6		0-99 (R FEEDB)		0-198 (TAP PAN)

7				0-99 (TAP FB)

8				0-99 (MASTER FB)

CONFIGURATION 4:

Not used

CONFIGURATION 6:

page

0 (type)	0 (MONO)	1 (STEREO)	2 (PING-PONG)

1	0-198 (IN MIX)	0-198 (IN MIX)	0-198 (IN MIX)

2	1-720 (DELAY)	1-320 (L DELAY)	1-320 (DELAY)

3	0-99 (FEEDB)	0-99 (L FEEDB)	0-99 (FEEDB)

4		1-320 (R DELAY)

5		0-99 (R FEEDB)

CONFIGURATION 7:

page

0	0-2 (SAMPLE PLAYBACK)

1	0-150 (SAMPLE START)

2	0-155 (SAMPLE LENGTH)

3	0-1 (AUDIO TRIG)

4	0-2 (MIDI TRIG)

5	0-127 (MIDI LOW LIMIT)

6	0-127 (MIDI BASE NOTE)

7	0-127 (MIDI HI LIMIT)

PITCH (FUNCTION 3)

CONFIGURATION 0 & 3:

page

0 (type)	0 (M CHORUS)	1 (S CHORUS)	2 (M FLANGE)	3 (S FLANGE)	4 (DETUNE)	5 (PHASER)

1	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)	0-1 (INPUT)

2	0-1 (WAVE)	0-1 (WAVE)	0-99 (SPEED)	0-99 (SPEED)	0-198 (TUNE)	0-99 (SPEED)

3	0-99 (SPEED)	0-99 (SPEED)	0-99 (DEPTH)	0-99 (DEPTH)		0-99 (DEPTH)

4	0-99 (DEPTH)	0-99 (DEPTH)	0-99 (FBACK)	0-99 (FBACK)

5	0-99 (FBACK)	0-99 (FBACK)	0-1 (TRIGGER)	0-1 (TRIGGER)

CONFIGURATION 1:

page

0	0-99 (SEPARATION)

1	0-1 (MOTOR)

2	0-1 (SPEED)

CONFIGURATION 2 & 7:

Not used

CONFIGURATION 4:

page

0 (type)	0 (CHORUS OFF)	1 (CHORUS ON)

1		0-1 (WAVE)

2		0-99 (SPEED)

3		0-99 (DEPTH)

CONFIGURATION 5:

page

0	1-300 (RING MOD SPECTRUM)

1	0-198 (RING MOD OUT MIX)

2	0-198 (RING MOD DEL/REV MIX)

CONFIGURATION 6:

page

0	0-1 (RESONATOR GATE MODE)

1	0-99 (RESONATOR DECAY)

2	0-60 (RESONATOR 1 TUNE)

3	0-60 (RESONATOR 2 TUNE)

4	0-60 (RESONATOR 3 TUNE)

5	0-60 (RESONATOR 4 TUNE)

6	0-60 (RESONATOR 5 TUNE)

EQ (FUNCTION 4)

CONFIGURATION 0 & 4:

page

0	20-999 (LOW FREQUENCY)

1	0-560 (LOW BOOST/CUT)

2	200-9999 (MID FREQUENCY)

3	20-255 (MID BANDWIDTH)

4	0-560 (MID BOOST/CUT)

5	2000-18000 (HIGH FREQUENCY)

6	0-560 (HIGH BOOST/CUT)

CONFIGURATION 1:

page

0	0-26 (HIGH ROTOR LEVEL)

CONFIGURATION 2:

page

0	0-28 (16Hz)

1	0-28 (32Hz)

2	0-28 (62Hz)

3	0-28 (126Hz)

4	0-28 (250Hz)

5	0-28 (500Hz)

6	0-28 (1KHz)

7	0-28 (2KHz)

8	0-28 (4KHz)

9	0-28 (8KHz)

10	0-28 (16KHz)

CONFIGURATION 3:

page

0	20-999 (LOW FREQUENCY)

1	0-560 (LOW BOOST/CUT)

2	20-500 (LOW MID FREQUENCY)

3	20-255 (LOW MID BANDWIDTH)

4	0-560 (LOW MID BOOST/CUT)

5	200-9999 (MID FREQUENCY)

6	20-255 (MID BANDWIDTH)

7	0-560 (MID BOOST/CUT)

8	2000-18000 (HIGH MID FREQUENCY)

9	20-255 (HIGH MID BANDWIDTH)

10	0-560 (HIGH MID BOOST/CUT)

11	2000-18000 (HIGH FREQUENCY)

12	0-560 (HIGH BOOST/CUT)

CONFIGURATION 5, 6 & 7:

Not used

CONFIGURATION (FUNCTION 7)

page

0	0-4 (CONFIGURATION)

0:  EQ>PCH>DL>REVERB

1:  LESLIE>DL>REVERB

2:  GRAPHIC EQ>DELAY

3:  5BAND EQ>PCH>DLY

4:  3 BAND EQ>REVERB

5:  RING>DL>REVERB

6:  RESONATOR>DL>REVERB

7:  SAMPLING

MIX (FUNCTION 8)

CONFIGURATION 0:

page

0 (type)	0 (PRE-EQ)	1 (POST-EQ)

1	0-99 (DIRECT)	0-99 (MAST FX)

2	0-99 (MAST FX)	0-99 (EQ)

3	0-99 (PITCH)	0-99 (PITCH)

4	0-99 (DELAY)	0-99 (DELAY)

5	0-99 (REVERB)	0-99 (REVERB)

CONFIGURATION 1:

page

0	0-99 (MAST FX)

1	0-99 (LESLIE)

2	0-99 (DELAY)

3	0-99 (REVERB)

CONFIGURATION 2:

page

0	0-99 (MAST FX)

1	0-99 (EQ)

2	0-99 (DELAY)

CONFIGURATION 3:

page

0 (type)	0 (PRE-EQ)	1 (POST-EQ)

1	0-99 (DIRECT)	0-99 (MAST FX)

2	0-99 (MAST FX)	0-99 (EQ)

3	0-99 (PITCH)	0-99 (PITCH)

4	0-99 (DELAY)	0-99 (DELAY)

CONFIGURATION 4:

page

0 (type)	0 (PRE-EQ)	1 (POST-EQ)

1	0-99 (DIRECT)	0-99 (MAST FX)

2	0-99 (MAST FX)	0-99 (EQ)

5	0-99 (REVERB)	0-99 (REVERB)

CONFIGURATION 5:

page

0	0-99 (MAST FX)

1	0-99 (DIRECT)

2	0-99 (RING MOD)

3	0-99 (DELAY)

4	0-99 (REVERB)

CONFIGURATION 6:

page

0	0-99 (MAST FX)

1	0-99 (DIRECT)

2	0-99 (RESONATOR)

3	0-99 (DELAY)

4	0-99 (REVERB)

CONFIGURATION 7:

page

0	0-99 (DIRECT)

1	0-99 (SAMPLE)

MOD (FUNCTION 9)

CONFIGURATION 0-6:

page

0	0-126 (MOD 1 SOURCE)

1	0-? (MOD 1 TARGET)

2	0-198 (MOD 1 AMPLITUDE)

3	0-126 (MOD 2 SOURCE)

4	0-? (MOD 2 TARGET)

5	0-198 (MOD 2 AMPLITUDE)

6	0-126 (MOD 3 SOURCE)

7	0-? (MOD 3 TARGET)

8	0-198 (MOD 3 AMPLITUDE)

9	0-126 (MOD 4 SOURCE)

10	0-? (MOD 4 TARGET)

11	0-198 (MOD 4 AMPLITUDE)

12	0-126 (MOD 5 SOURCE)

13	0-? (MOD 5 TARGET)

14	0-198 (MOD 5 AMPLITUDE)

15	0-126 (MOD 6 SOURCE)

16	0-? (MOD 6 TARGET)

17	0-198 (MOD 6 AMPLITUDE)

18	0-126 (MOD 7 SOURCE)

19	0-? (MOD 7 TARGET)

20	0-198 (MOD 7 AMPLITUDE)

21	0-126 (MOD 8 SOURCE)

22	0-? (MOD 8 TARGET)

23	0-198 (MOD 8 AMPLITUDE)

CONFIGURATION 7:

Not used

Modulation target values are dependent on the current configuration and mode of a program.  The most significant nibble determines the function being modulated as follows:

0XH:	REVERB MOD

1XH:	DELAY MOD

2XH:	PITCH MOD

3XH:	EQ MOD

4XH:	MIX MOD

5XH:	MULTI-TAP MOD (Configuration 3 only)

6XH:	   "    "     "     "           "   "   "     "   "

The possible modulation targets within each of the above is as follows:

REVERB CONFIGURATION 0,1,4,5,6 (nothing in 2, 3, & 7):

Target	PLATE	ROOM	CHAMBER	HALL	REVERSE

00H	IN MIX	IN MIX	IN MIX	IN MIX	IN MIX

01H	PREDLY	PREDLY	PREDLY	PREDLY	PREDLY

02H	PRE MIX	PRE MIX	PRE MIX	PRE MIX	PRE MIX

03H	DECAY	DECAY	DECAY	0DECAY	REV TIME

04H	DIFFUSION	DIFFUSION	DIFFUSION	DIFFUSION	DIFFUSION

05H	DENSITY	DENSITY	DENSITY	LOW DEC	DENSITY

06H	LOW DEC	LOW DEC	LOW DEC	HIGH DEC	LOW DEC

07H	HIGH DEC	HIGH DEC	HIGH DEC		HIGH DEC

DELAY CONFIGURATION 0,1 (nothing in 4 & 7):

Target	MONO	STEREO	PING-PONG

10H	IN MIX	IN MIX	IN MIX

11H	DELAY	L DELAY	DELAY

12H	FEEDB	L FEEDB	FEEDB

13H		R DELAY

14H		R FEEDB

CONFIGURATION 3:

Target	MONO	STEREO	PING-PONG	MULTI-TAP

10H	IN MIX	IN MIX	IN MIX	IN MIX

11H	DELAY	L DELAY	DELAY	TAP 1 DELAY

12H	FEEDB	L FEEDB	FEEDB	TAP 2 DELAY

13H		R DELAY		TAP 3 DELAY

14H		R FEEDB		TAP 4 DELAY

15H				TAP 5 DELAY

16H				TAP 6 DELAY

17H				TAP 7 DELAY

18H				TAP 8 DELAY

50H				TAP 1 VOLUME

51H				TAP 2 VOLUME

52H				TAP 3 VOLUME

53H				TAP 4 VOLUME

54H				TAP 5 VOLUME

55H				TAP 6 VOLUME

56H				TAP 7 VOLUME

57H				TAP 8 VOLUME

58H				TAP 1 PANNING

59H				TAP 2 PANNING

5AH				TAP 3 PANNING

5BH				TAP 4 PANNING

5CH				TAP 5 PANNING

5DH				TAP 6 PANNING

5EH				TAP 7 PANNING

5FH				TAP 8 PANNING

60H				TAP 1 FEEDBACK

61H				TAP 2 FEEDBACK

62H				TAP 3 FEEDBACK

63H				TAP 4 FEEDBACK

64H				TAP 5 FEEDBACK

65H				TAP 6 FEEDBACK

66H				TAP 7 FEEDBACK

67H				TAP 8 FEEDBACK

68H				MASTER FEEDBACK

CONFIGURATION 2,5,6:

Target	MONO	STEREO	PING-PONG

10H	DELAY	L DELAY	DELAY

11H	FEEDB	L FEEDB	FEEDB

12H		R DELAY

13H		R FEEDB

PITCH CONFIGURATION 0 & 3 (nothing in 2 & 7):

Target	M CHORUS	S CHORUS	M FLANGE	S FLANGE	DETUNE	PHASER

20H	SPEED	SPEED	SPEED	SPEED	DETUNE	SPEED

21H	DEPTH	DEPTH	DEPTH	DEPTH		DEPTH

22H	FBACK	FBACK	FBACK	FBACK

CONFIGURATION 1:

Target

20H	SEPARATION

21H	MOTOR

22H	SPEED

CONFIGURATION 4:

Target

20H	SPEED

21H	DEPTH

CONFIGURATION 5:

Target

20H	SPECTRUM SHIFT

21H	RING OUTPUT MIX

22H	DEL/REV IN MIX

CONFIGURATION 6:

Target

20H	RESONATOR DECAY

EQ CONFIGURATION 0 & 4 (nothing in 5, 6, & 7):

Target

30H	LOW FREQUENCY

31H	LOW BOOST/CUT

32H	MID FREQUENCY

33H	MID BANDWIDTH

34H	MID BOOST/CUT

35H	HIGH FREQUENCY

36H	HIGH BOOST/CUT

CONFIGURATION 1:

Target

30H	HIGH ROTOR LEVEL

CONFIGURATION 2:

Target

30H	16Hz

31H	32Hz

32H	62Hz

33H	126Hz

34H	250Hz

35H	500Hz

36H	1KHz

37H	2KHz

38H	4KHz

39H	8KHz

3AH	16KHz

CONFIGURATION 3:

Target

30H	LOW FREQUENCY

31H	LOW BOOST/CUT

32H	LOW MID FREQUENCY

33H	LOW MID BANDWIDTH

34H	LOW MID BOOST/CUT

35H	MID FREQUENCY

36H	MID BANDWIDTH

37H	MID BOOST/CUT

38H	HIGH MID FREQUENCY

39H	HIGH MID BANDWIDTH

3AH	HIGH MID BOOST/CUT

3BH	HIGH FREQUENCY

3CH	HIGH BOOST/CUT

MIX CONFIGURATION 0:

Target	PRE-EQ	POST-EQ

40H	DIRECT	MAST FX

41H	MAST FX	EQ

42H	PITCH	PITCH

43H	DELAY	DELAY

44H	REVERB	REVERB

CONFIGURATION 1:

Target

40H	MAST FX

41H	LESLIE

42H	DELAY

43H	REVERB

CONFIGURATION 2:

Target

40H	MAST FX

41H	EQ

42H	DELAY

CONFIGURATION 3:

Target

40H	DIRECT

41H	MAST FX

42H	PITCH

43H	DELAY

CONFIGURATION 4:

Target

40H	DIRECT

41H	MAST FX

42H	REVERB

CONFIGURATION 5:

Target

40H	DIRECT

41H	MAST FX

42H	RING MOD

43H	DELAY

44H	REVERB

CONFIGURATION 6:

Target

40H	DIRECT

41H	MAST FX

42H	RESONATOR

43H	DELAY

44H	REVERB

NAME (FUNCTION 10)

CONFIGURATION 0-4:

page

0	32-127 (1st DIGIT NAME)

1	32-127 (2nd DIGIT NAME)

2	32-127 (3rd DIGIT NAME)

3	32-127 (4th DIGIT NAME)

4	32-127 (5th DIGIT NAME)

5	32-127 (6th DIGIT NAME)

6	32-127 (7th DIGIT NAME)

7	32-127 (8th DIGIT NAME)

8	32-127 (9th DIGIT NAME)

9	32-127 (10th DIGIT NAME)

10	32-127 (11th DIGIT NAME)

11	32-127 (12th DIGIT NAME)

12	32-127 (13th DIGIT NAME)

13	32-127 (14th DIGIT NAME)

PARAMETER ADDRESSES WITHIN PROGRAMS

The following addresses are relative to the first address of a program.  These addresses assume that the data has been unpacked into byte values.  Blank locations should be left 0.

00	LOW EQ FREQ MSB

01	LOW EQ FREQ LSB / 16Hz

02	LOW EQ AMP MSB / 32Hz

03	LOW EQ AMP LSB / 62Hz

04	MID EQ FREQ MSB / 126Hz

05	MID EQ FREQ LSB / 250Hz

06	MID EQ BANDWIDTH / 500Hz

07	MID EQ AMP MSB / 1KHz

08	MID EQ AMP LSB / 2KHz

09	HIGH EQ FREQ MSB / 4KHz

0A	HIGH EQ FREQ LSB / 8KHz

0B	HIGH EQ AMP MSB / 16KHz

0C	HIGH EQ AMP LSB

0D	LESLIE HIGH ROTOR LEVEL / TAP 1 DELAY MSB

0E	LOW MID EQ FREQ MSB

0F	LOW MID EQ FREQ LSB

10	LOW MID EQ BANDWIDTH

11	LOW MID EQ AMP MSB

12	LOW MID EQ AMP LSB

13	HIGH MID EQ FREQ MSB

14	HIGH MID EQ FREQ LSB

15	HIGH MID EQ BANDWIDTH

16	HIGH MID EQ AMP MSB

17	HIGH MID EQ AMP LSB

18	SAMPLE START / TAP 1 DELAY LSB

19	SAMPLE LENGTH / TAP 1 VOLUME

1A	PITCH MODE

1B	PITCH INPUT

1C	LFO WAVEFORM

1D	LFO SPEED

1E	LFO DEPTH / RESONATOR DECAY

1F	SAMPLE PLAYBACK MODE / TAP 1 PAN

20	PITCH FEEDBACK

21	DETUNE AMOUNT / SAMPLE PITCH

22	LESLIE SEPARATION / TAP 1 FEEDBACK

23	LESLIE MOTOR / SAMPLE REC AUDIO TRIG /

TAP 2 DELAY MSB

24	LESLIE SPEED / SAMPLE MIDI TRIG /

TAP 2 DELAY LSB

25	TRIGGER FLANGE / RES MIDI GATE

26	SAMPLE MIDI BASE NOTE / TAP 2 VOLUME

27	DELAY MODE

28	DELAY INPUT

29	DELAY INPUT MIX

2A	DELAY MSB / LEFT DELAY MSB / TAP 2 PAN

2B	DELAY LSB / LEFT DELAY LSB /TAP 2 FEEDBACK

2C	FEEDBACK / LEFT FEEDBACK / TAP 3 DELAY MSB

2D	RIGHT DELAY MSB / TAP 3 DELAY LSB

2E	RIGHT DELAY LSB / TAP 3 VOLUME

2F	RIGHT FEEDBACK / TAP 3 PAN

30	SAMPLE LOW MIDI NOTE / TAP 3 FEEDBACK

31	SAMPLE HIGH MIDI NOTE / TAP 4 DELAY MSB

32	REVERB MODE / TAP 4 DELAY LSB

33	TAP 4 VOLUME

34	REVERB INPUT 1 / TAP 4 PAN

35	REVERB INPUT 2 / TAP 4 FEEDBACK

36	REVERB INPUT MIX / TAP 5 DELAY MSB

37	REVERB PREDELAY / TAP 5 DELAY LSB

38	REVERB PREDELAY MIX / TAP 5 VOLUME

39	REVERB DECAY / TAP 5 PAN

3A	REVERB DIFFUSION / TAP 5 FEEDBACK

3B	REVERB LOW DECAY / TAP 6 DELAY MSB

3C	REVERB HIGH DECAY / TAP 6 DELAY LSB

3D	REVERB DENSITY / TAP 6 VOLUME

3E	REVERB GATE / TAP 6 PAN

3F	REVERB GATE HOLD / TAP 6 FEEDBACK

40	REVERB GATE RELEASE / TAP 7 DELAY MSB

41	REVERB GATED LEVEL / TAP 7 DELAY LSB

42	RING MOD SHIFT MSB / TAP 7 VOLUME

43	RING MOD SHIFT LSB / TAP 7 PAN

44	CONFIGURATION

45	PRE (00), POST (01), POST PANNING (10), POST TREMOLO (11)

46	DIRECT LEVEL / EQ LEVEL

47	MASTER EFFECTS LEVEL

48	PITCH LEVEL / LESLIE LEVEL / RING MOD LEV

49	DELAY LEVEL

4A	REVERB LEVEL

4B	RESONATOR PITCH 1 / TAP 8 DELAY MSB

4C	RESONATOR PITCH 2 / TAP 8 DELAY LSB

4D	RESONATOR PITCH 3 / TAP 8 VOLUME

4E	RESONATOR PITCH 4 / TAP 8 PAN

4F	RESONATOR PITCH 5 / TAP 8 FEEDBACK

50	MOD 1 SOURCE

51	MOD 1 TARGET

52	MOD 1 AMPLITUDE

53	MOD 2 SOURCE

54	MOD 2 TARGET

55	MOD 2 AMPLITUDE

56	MOD 3 SOURCE

57	MOD 3 TARGET

58	MOD 3 AMPLITUDE

59	MOD 4 SOURCE

5A	MOD 4 TARGET

5B	MOD 4 AMPLITUDE

5C	MOD 5 SOURCE

5D	MOD 5 TARGET

5E	MOD 5 AMPLITUDE

5F	MOD 6 SOURCE

60	MOD 6 TARGET

61	MOD 6 AMPLITUDE

62	MOD 7 SOURCE

63	MOD 7 TARGET

64	MOD 7 AMPLITUDE

65	MOD 8 SOURCE

66	MOD 8 TARGET

67	MOD 8 AMPLITUDE

68	MULTITAP MASTER FEEDBACK

69	MULTITAP NUMBER

6A	1ST DIGIT NAME

6B	2ND DIGIT NAME

6C	3RD DIGIT NAME

6D	4TH DIGIT NAME

6E	5TH DIGIT NAME

6F	6TH DIGIT NAME

70	7TH DIGIT NAME

71	8TH DIGIT NAME

72	9TH DIGIT NAME

73	10TH DIGIT NAME

74	11TH DIGIT NAME

75	12TH DIGIT NAME

76	13TH DIGIT NAME

77	14TH DIGIT NAME

78	RING MOD OUTPUT MIX

79	RING MOD DEL/REV MIX

7A	PAN SPEED

7B	PAN DEPTH

7C-7F (blank)